## Slide 1
Industry’s First 3-Stream
802.11n Competitive Testing
October, 2012
Notes: Overview presentation + detailed notes

## Slide 2: Starting at the End (Key Findings)
Independent testing performed by Syracuse University at Syracuse University (Ruckus did not pay for testing)
Ruckus worked with SU on test bed but not allowed to influence actual testing
Wide variations between vendor claims and actual performance of 3-stream 802.11n APs (surprise, surprise)
At distance and as environment becomes difficult (e.g. more clients, interference), AP performance degrades
Ruckus doesn’t win all tests but delivers overall best TCP performance and client capacity

## Slide 3: Test Overview
Goal: Determine real-world 3-stream AP performance via independent testing at Syracuse
Industry’s first competitive testing of three-stream capable 802.11n enterprise APs
Three tests performed:
  Single AP, single client
  Single AP, multiple clients
  Multiple APs multiple clients
Aerohive
330
Aruba
135
Cisco
3602i
Meraki
24
Ruckus
7982

## Slide 4: Overall Vendor Performances
Chart: 
| 1st Qtr | 2nd Qtr | 3rd Qtr | 4th Qtr
Sales | 66 | 14 | 12 | 2.3 | 5.7
Percentage of Vendor Test Wins
(87 tests)
Industry’s First 3x3:3 802.11n Competitive Testing
66%
14%
12%
2%
6%

## Slide 5: Overall Vendor Performances
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 83 | 17
Multi-Client Tests
(12 tests)
Industry’s First 3x3:3 802.11n Competitive Testing
83%
17%
0%
Chart: 
| 1st Qtr | 2nd Qtr
Sales | 58 | 32 | 3 | 3 | 3
Multi-AP Tests
(30 tests)
58%
32%
3%
3%

## Slide 6: Test Methodology
What is it?
Testing in an environment that closely resembles actual customer deployment and environment
Focus on most deployments are capacity-based, not coverage
Why do it?
One client/one AP does not guarantee a successful, multi-client deployment
Vendor claims ≠ actual throughput
Goals
Show real, meaningful, achievable performance

## Slide 7: Cross-Test Constants
Very clean RF environment (tests performed at night)
3-stream MacBook Pros and NETGEAR USBs dongles
IxChariot: Throughput.scr
    1MB file transfer for 2 minutes
    High Performance Throughput script for single AP tests
    10MB file transfer for 2 minutes
20MHz channel width for 2.4GHz, 40MHz for 5GHz
AP channel selection
  Single AP: ch. 1 (2.4 GHz), ch 36 (5 GHz)
  Multi AP: automated channel selection, then set manually
“Winner” determined by aggregate TCP throughput

## Slide 8: Hinds Hall

## Slide 9: Wi-Fi Test Overview
Single AP, single client per radio at various distances
  2.4 GHz, 5 GHz, 2.4 GHz and 5 GHz
  135 tests for each AP (5 locations, “3” bands, 3 orientation, up/down/bi)
Single AP, multiple clients
  One AP, three rooms, 30 clients/room
  Rooms are different distances away from AP
  2.4 GHz, 5 GHz, 2.4 GHz and 5 GHz
Multi-AP, multi-client
  1 - 4 rooms of 30 clients (120 clients)
  Channel selection, client load balancing, band steering all enabled
  Tests with and without an interfering Wi-Fi neighbor network

## Slide 10: Test 1: Single AP Single Client
5 locations of varied distances and difficulties
2.4 GHz, 5GHz, simultaneous
Up/down/bi-directional
3 orientations
AP
1
2
3
4
5
58’ from AP
30’ from AP
40’ from AP
24’ from AP
105’ from AP
Client locations
  = 135 (5 * 3 * 3 * 3) tests for each vendor’s AP
HINDS
HALL

## Slide 11: Single AP, Single Client Performance
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 372 | 368 | 320 | 260 | 192
Aerohive
330
Aruba
135
Cisco
3602i
Meraki
24
Ruckus
7982
372
368
320
260
192
BI-DIRECTIONAL
TCP THROUGHPUT
FOR DUAL BAND CLIENTS
SHORT DISTANCE
Location 4, 24’ (7.3M)
Average of three discrete runs (client rotated each time) with two clients (each transmitting and receiving on different bands)
1
2
2.4 GHz
5 GHz
Mbps
Notes: One Ruckus run was 390

## Slide 12: Aruba 135 vs. ZoneFlex 7982
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 162.5 | 227.1 | 202 | 241.1 | 130.8
Aruba | 157.9 | 222.8 | 168 | 227.3 | 90
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 157 | 210.3 | 194.7 | 213 | 132.7
Aruba | 150.3 | 215.6 | 157.8 | 234.9 | 87.8
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 99.2 | 137.2 | 125.4 | 146.7 | 102.4
Aruba | 104.5 | 131 | 129.5 | 134.4 | 92.3
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 100.3 | 143.3 | 142.8 | 140.4 | 119.6
Aruba | 98.2 | 145.9 | 140.3 | 136.2 | 99.6
2.4GHz
5GHz
2.4GHz
5GHz
5GHz
2.4GHz
DOWN
UP
vs.
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 97.8 | 146.5 | 142.5 | 145 | 116.2
Aruba | 97.6 | 145.9 | 136.4 | 136.4 | 96.6
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 185.2 | 249.4 | 217.3 | 224.5 | 123.2
Aruba | 177.6 | 138.5 | 140.8 | 220.7 | 114.1
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
LOCATIONS
1 2 3 4 5
Both

## Slide 13: Cisco 3602i vs. ZoneFlex 7982
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 185.2 | 249.4 | 217.3 | 224.5 | 123.2
Cisco | 69.5 | 126.5 | 105.6 | 164.1 | 56.1
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 99.2 | 137.2 | 125.4 | 146.7 | 102.4
Cisco | 99.9 | 125.6 | 117.4 | 119.4 | 83
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 97.8 | 146.5 | 142.5 | 145 | 116.2
Cisco | 70.6 | 114.4 | 112.8 | 108.1 | 85.8
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 100.3 | 143.3 | 142.8 | 140.4 | 119.6
Cisco | 67.4 | 108.7 | 104.4 | 97.3 | 88.5
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 162.5 | 227.1 | 202 | 241.1 | 130.8
Cisco | 56.6 | 166.5 | 107.3 | 268.8 | 55.1
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 157 | 210.3 | 194.7 | 213 | 132.7
Cisco | 50.7 | 157 | 97.2 | 243 | 55.2
2.4GHz
5GHz
2.4GHz
5GHz
5GHz
2.4GHz
DOWN
UP
Both
vs.
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
LOCATIONS

## Slide 14: Aerohive 330 vs. ZoneFlex 7982
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 157 | 210.3 | 194.7 | 213 | 132.7
Aerohive | 101.3 | 189.9 | 119.1 | 226.2 | 92.8
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 162.5 | 227.1 | 202 | 241.1 | 130.8
Aerohive | 100.3 | 193.4 | 123.4 | 234 | 93.2
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 99.2 | 137.2 | 125.4 | 146.7 | 102.4
Aerohive | 52.2 | 64.3 | 60.2 | 124.5 | 42.9
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 97.8 | 146.5 | 142.5 | 145 | 116.2
Aerohive | 83.6 | 131.2 | 124.9 | 136.8 | 88.2
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 185.2 | 249.4 | 217.3 | 224.5 | 123.2
Aerohive | 102.7 | 168.8 | 136.4 | 230.7 | 93.2
2.4GHz
5GHz
2.4GHz
5GHz
5GHz
2.4GHz
DOWN
UP
Both
vs.
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 100.3 | 143.3 | 142.8 | 140.4 | 119.6
Aerohive | 92 | 133.4 | 133.2 | 135.3 | 112.1
1 2 3 4 5
1 2 3 4 5
LOCATIONS
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5

## Slide 15: Meraki 24 vs. ZoneFlex 7982
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 162.5 | 227.1 | 202 | 241.1 | 130.8
Meraki | 52.6 | 237 | 226.7 | 222.3 | 108.6
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 185.2 | 249.4 | 217.3 | 224.5 | 123.2
Meraki | 44.5 | 225.1 | 205.2 | 193.8 | 96.8
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 97.8 | 146.5 | 142.5 | 145 | 116.2
Meraki | 59.2 | 107.7 | 94.2 | 91.2 | 63.6
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 99.2 | 137.2 | 125.4 | 146.7 | 102.4
Meraki | 18.3 | 88.5 | 69.4 | 66.8 | 36.4
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 100.3 | 143.3 | 142.8 | 140.4 | 119.6
Meraki | 83.5 | 112.5 | 104.3 | 93.5 | 83.2
Chart: 
| loc 1 | loc 2 | loc 3 | loc 4 | loc 5
Ruckus | 157 | 210.3 | 194.7 | 213 | 132.7
Meraki | 46.4 | 232.9 | 227.2 | 228.6 | 114.5
2.4GHz
5GHz
2.4GHz
5GHz
5GHz
2.4GHz
DOWN
UP
Both
vs.
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
LOCATIONS

## Slide 16: Single AP, Single Client Performance
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 275 | 274 | 184 | 159 | 68
Aerohive
330
Aruba
135
Cisco
3602i
Meraki
24
Ruckus
7982
275
274
184
159
68
Location 1 ,58’ (17.7m)
Mbps
BI-DIRECTIONAL
TCP THROUGHPUT
FOR DUAL BAND CLIENTS
MEDIUM DISTANCE
1
2
2.4 GHz
5 GHz

## Slide 17: Single AP, Single Client Performance
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 228 | 183 | 142 | 107 | 44
Aerohive
330
Aruba
135
Cisco
3602i
Meraki
24
Ruckus
7982
228
184
142
107
44
Location 5, 105’ (32m)
BI-DIRECTIONAL
TCP THROUGHPUT
FOR DUAL BAND CLIENTS
LONG DISTANCE
Mbps
1
2
2.4 GHz
5 GHz

## Slide 18: Test 2: Single AP, Multi-Client
One AP, three rooms, 30 clients/room
Mixed bands (⅓ on 2.4 GHz | ⅔ on 5 GHz) + bi-directionality
All clients associated, even if not being tested
Room 1: 20’ from AP
  30 PCs with dongles
Room 2: 45’ from AP
  30 MacBook Pros
Room 3: 55’ from AP
  30 PCs with dongles
All rooms, 90 clients across all 3 rooms simultaneously
AP
1
2
3
Center of room
30 evenly distributed clients

## Slide 19: Single AP, Multi-Client, Room 1
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 206 | 183 | 180 | 128 | 99
Aruba
135
Cisco
3602i
Meraki
24
Ruckus
7982
206
183
180
128
99
Aerohive
330
20’ (3m)
BI-DIRECTIONAL
TCP THROUGHPUT
1 AP, 1 ROOM, 30 CLIENTS
SHORT DISTANCE
Mbps

## Slide 20: Single AP, Multi-Client, Room 2
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 143 | 119 | 71 | 71 | 18
Aerohive
330
Aruba
135
Cisco
3602i
Meraki
24
Ruckus
7982
143
119
71
71
18
45’ (15m)
Mbps
BI-DIRECTIONAL
TCP THROUGHPUT
1 AP, 1 ROOM, 30 CLIENTS
MEDIUM DISTANCE

## Slide 21: Single AP, Multi-Client, Room 3
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 91 | 63 | 31 | 25 | 1
Cisco
3602i
Aruba
135
Aerohive
330
Meraki
24
Ruckus
7982
91
63
31
25
0
60’ (18m)
Mbps
BI-DIRECTIONAL
TCP THROUGHPUT
1 AP, 1 ROOM, 30 CLIENTS
LONG DISTANCE

## Slide 22: High Density TCP Performance
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 130 | 77 | 56 | 39 | 0
Aerohive
330
Aruba
135
Cisco
3602i
Meraki
24
Ruckus
7982
130
77
56
39
0
BI-DIRECTIONAL
TCP THROUGHPUT
1 AP, 3 ROOMS, 90 CLIENTS
ALL DISTANCES
Mbps

## Slide 23: Test 3: Multiple APs, Multiple Clients
6 APs, 4 rooms
Each classrooms has an AP, 30 clients (120 clients total)
  Clients: ⅓ on 2.4 GHz, ⅔ on 5 GHz
2 other APs in nearby rooms
  Features turned on:
    Auto channel selection
    Client load balancing
    Airtime fairness
  Room 1: 30 PCs w/ Netgear dongles
  Room 2: 24 MacBooks, 6 Dell laptops
  Room 3: 30 PCs w/ Netgear dongles
  Room 4: 30 PCs w/ Linksys dongles
Test with and without nearby rogue Wi-Fi network (interferer)
  Two PCs running iPerf for the duration of the testing
1
2
3
Classrooms
AP
AP
AP
AP
AP
AP
4
R

## Slide 24: Multiple APs, Multiple Clients
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Series 1 | 562 | 480 | 378 | 330 | 323
Aerohive
330
Aruba
135
Cisco
3602i
Meraki
24
Ruckus
7982
562
480
378
324
330
BI-DIRECTIONAL
TCP THROUGHPUT
6 APs, 120 CLIENTS
NO NEIGHBOR APS
Mbps
24 clients uploading (8 on 2.4 and 16 on 5GHz)
96 clients downloading (32 on 2.4 and 64 on 5 GHz)

## Slide 25: Multiple APs, Multiple Clients
Chart: 
| Category 1 | ah | Category 3 | Category 4
Series 1 | 570 | 441 | 374 | 369 | 324
Aerohive
330
Aruba
135
Cisco
3602i
Meraki
24
Ruckus
7982
570
441
374
369
324
BI-DIRECTIONAL
TCP THROUGHPUT
6 APs, 120 CLIENTS
WITH NEIGHBOR AP
Mbps
ROGUE AP
Dual-band AP with two 2.4GHz laptops associated client transmitting data back and forth broadcasting on same channel (6) and 5 GHz radio broadcasting
with no clients

## Slide 26: Summary
Three-stream 802.11n won’t deliver what vendors promise
Rigorous testing methodology is essential
  Single AP----client testing doesn’t give full picture
  Multi-AP-----multi client tests reflect more real world
  Hundreds of tests required to determine the truth
  Designing repeatable tests is essential
  Ensuring all SSIDs are the same across vendors
  Getting PC clients associated
(Dis)advantages of cloud controller
The ZF 7982 is a fancy piece of kit
  Consistently very consistent and high performing

## Slide 27: The Syracuse Test Team